Embedded System
Francesco De Patre – 382760
# Introduction
The second lab focuses on direct interaction with hardware through General-Purpose Input/Output (GPIO), used to manage digital input and output signals. Specifically, the mechanisms for controlling an LED and reading the state of a button are analyzed.
A central aspect of the lab is understanding the devicetree, which is the level of abstraction Zephyr uses to describe hardware.
This approach allows you to separate application logic from platform-specific details, improving code portability.
Furthermore, the lab introduces two different approaches to input management: polling and interrupts. Comparing these two techniques highlights important trade-offs in terms of efficiency, energy consumption, and system responsiveness.

# Methodology
The lab was approached by first analyzing the hardware configuration using devicetree and then implementing different ways of interacting between input (button) and output (LED). Different approaches (polling and interrupt) were compared through incremental code changes.
# LAB Section
## Technical objective
Understand the use of GPIOs and the Zephyr driver model, analyzing different strategies for handling inputs.
## What was done during the laboratory
LED control via a button was implemented, first using polling and then using interrupts. The configuration was also modified to use a different LED.
## What can be understood
This lab highlighted the role of the devicetree as a hardware abstraction layer.

Furthermore, the comparison between polling and interrupts clearly showed the trade-offs:
- polling → simple but inefficient
- interrupt → more efficient and responsive
## Problems encountered
The problems encountered mainly concern the difficulty in understanding the device tree, the management of GPIO configurations and unexpected initial behavior of interrupts.
## Possible improvements
Use only interrupts in real systems to reduce power consumption and improve responsiveness.
## Evidence

## Task
The polling method requires the CPU to periodically check the button's state, even when no events are present. This consumes unnecessary power and introduces a delay between input and response, making it inefficient, especially in low-power systems.
Furthermore, to turn the LED on when pressed and off when released, you need to: configure the LED as initially off and generate interrupts on both sides (press and release)
This way the system reacts to both events without continuous polling.
# GenAI Statement
Generative AI tools were used to support study and writing during the workshops and in the preparation of this report.

In particular, these tools have been used to:
- improve the presentation quality of the report, making the text clearer, more structured and coherent;
- facilitate understanding of the technical documentation relating to the various course modules (e.g. nRF Connect SDK and Toolchain);
- support the translation and reformulation of content, in order to obtain more precise technical terminology;
- assist in solving practical problems, particularly related to compatibility between the system used (personal computer), the software tools and the board used in the laboratories.
All content generated with the support of GenAI tools has been critically reviewed, verified, and adapted based on personal understanding of the topics covered.